## Slide 1: WIPR -- a Public Key Implementation on Two Grains of Sand
Yossi Oren1, Martin Feldhofer2
1Weizmann Institute of Science
2Graz University of Technology
Notes: At 2003 we thought PK would not fit on RFID
Currently the state of the art is either:
Weak PK for cheap devices
Strong PK for expensive devices
Taking it to the next level…

## Slide 2: Not watered down
1024-bit public key
Full encryption
5705 gates, including RAM and ROM
600ms/10µA at 100KHz
Works great with the EPC C1G2 standard
Notes: This is not a watered down version of public key
Or the “mobile version” of public key

## Slide 3: Talk Outline
What inventory applications gain from PK
The WIPR PK scheme in theory
Implementation results
Integration with EPC

## Slide 4: Inventory + PK encryption = awesome
Addictol 50mg
#6382020
200 € Bill
#426144
U.S. Passport
#1800400400
Notes: Inventory applications: identity providing vs identity proving – reader has never seen the tag before
Examples:
Supply chain
Medicine
Passports
Money
Related field: sensor networks
This is what it looks like if you have the PK

## Slide 5: Inventory + PK encryption = awesome
WIPR version 1
WIPR version 1
WIPR version 1
Secrecy (and anti-counterfeiting)
Metadata privacy
Full backward and forward privacy
Implicit reader authentication
Works even if tag is completely compromised!
Notes: Secrecy: cannot learn anything about the ID of an unknown tag.
Metadata privacy: The adversary cannot determine whether a certain public key n was used in the protocol exchange.
Full privacy: cannot determine whether a tag was a part of any past or future protocol exchange - Very useful for banknotes
Implicit Reader Authentication: secure data channel from the reader to the tag
(that’s the magic of PK)

## Slide 6: WIPR in Theory
Rabin’s scheme [R79, GM82]:
  Private Key: primes p,q. Public Key: n=p¢q
  Encryption: C=P2(mod n)
Low-resource version [N92, S94]:
  Encryption: C=P2+r¢n, random r
  Statistically indistinguishable from Rabin’s scheme when r is appropriately chosen
Super-low-resource version (this work):
  Specially-formed n stored within 200 GEs
  Long random strings created on-the-fly using Feistel structure
Notes: Shafi Goldwasser and Silvio Micali. STOC '82
M. Rabin. MIT TR, 1979.
Adi Shamir. EUROCRYPT '94
Naccache patent application 92 and Eurocrypt 95

## Slide 7: The WIPR Protocol
Plaintext is expanded to n bits, then squared using a standard multiply-accumulator

## Slide 8: Imlementation Details
Encryption: C=(ID,rr,rt1)2+rt2¢n

## Slide 9: Implementation Results
Chart: WIPR
Chart: Implementation Cost (GEs)
| WIPR-1024 | AES-128 [FDW04] | ECC-192 [FW07] | NTRU-57 [GKS04] | GPS-160 [McLR07]
Combinational | 2860 | 1220 | 12080 | 523 | 1541
RAM+ROM | 2845 | 2375 | 11520 | 2327 | 7099
Notes: Show of hands
GPS: M. McLoone and M.J.B. Robshaw, Public Key Cryptography and RFID Tags, CT-RSA 2007
NTRU: Gunnar Gaubatz, Jens-Peter Kaps, Berk Sunar, ESAS 2004
ECC: Furbass, F.; Wolkerstorfer, J, ISCAS 2007
AES: M. Feldhofer, S. Dominikus, and J. Wolkerstorfer. CHES 2004
David Molnar David Wagner – CCS 2004

## Slide 10: Integration with EPC C1G2
WIPR ciphertext ¼ 2048 bits in 600ms
C1G2 data rate ¼ 50 kbps
How do we maximize the interrogation rate?

## Slide 11: Integration with EPC C1G2
Crucial for the security of the scheme

## Slide 12: Thank you!
For more information:
http://iss.oy.ne.ro/WIPR
Notes: Explore security paramaters
Physical implementation of WIPR on a real + reader

## Slide 13: WIPR and other PK Schemes
When comparing the gate cost of WIPR to another scheme, don’t forget to check:
  Does the gate cost include RAM and ROM?
  Does it use a full-strength cipher or a “mobile version”?
  Does it do encryption? Does it support secrecy and privacy?
  Is it a full scheme, or only a cryptographic construct?